## Slide 1: SNS COLLEGE OF TECHNOLOGY
An Autonomous Institution Coimbatore-35
Department of Artificial Intelligence and Data Science
23EET103-Electric Circuits and Electron Devices.
UNIT III :WIRING, GROUNDING AND SAFETY
I B.TECH AIDS / I SEMESTER
Topic 1 : Wiring: General Rules , Materials and
Accessories
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 2: Let’s Recall !!
2/25
What is wiring?
Why do we need rules for safe wiring? Common household wiring components Difference between good and faulty wiring What are electrical materials?
Why are wiring accessories needed in installations?
Basic components used in home wiring
Conductors, insulators, and their importance
Safety devices used in wiring systems
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 3: TOPICS FOR DISCUSSION
3/25
Why Wiring Rules?
General Rules for Electrical Wiring Types of Wiring Systems
Common Wiring Terminologies Real-world Need for Proper Wiring
Materials used in electrical wiring
Types of wiring accessories
Role of each accessory in wiring
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 4: ELECTRICAL WIRING
Electrical wiring is process of connecting cables and wires to the related devices such as Fuse, sockets, fans, lights etc.. to the main distribution boards is a specific structure for continues supply.
4/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 5: RULES OF ELECTRICAL WIRING
The total lighting load in a sub circuit should not be more than 100W.
Every fitting or appliance must be controlled by switch.
Every socket outlet must be controlled by switch.
The switch should be on the line conductor.
5/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 6: WIRING ACCESSORIES AND MATERIALS
Cables
Flexible wires
Switches
Fuses
Ceiling rose
Lamp holders
Plugs
Socket outlets
Junction boxes
6/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 7: CABLES
A cable is made of some conducting material such as copper or aluminium. It is surrounded by insulation and a sheath for mechanical protection.
The cables are generally classified
to the insulation used.
types of cables are as
according Different follows:
Weather- proof cables
Polyvinyl chloride insulated cables (PVC)
Lead sheathed cables
Cab tyre sheathed cables (CTS)
7/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 8: FLEXIBLE CORD
In the flexible cord, a large number of fine wires are used to form the conductor. These are insulated by plastic insulation.
The flexible cords are used as connecting wires to connect the portable domestic appliances and light fittings etc.
8/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 9: SWITCHES
Tumbler switch
Flush switch
9/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 10: SURFACE OR TUMBLER SWITCH
••Single-way switch
••Two-way switch
10/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 11: PULL SWITCHES OR CEILING SWITCHES
The Pull switches are fixed on the ceiling and all live parts are out of reach of the operator
The switch has strong mechanical action. It is operated with a single pull.
11/25
11/22/2025
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 12: ROTARY SNAP SWITCH
12/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 13: PUSH BUTTON SWITCH
This type of switch consists of one blade only.
The blade is given a rocking action by press button and movement is controlled by a cam and spring.
13/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 14: FUSES
In any electrical installation, fuse is used for protecting the appliances against over current. Fuse is used in different stages of the wiring.
A fuse can be made of the
conducting
following materials:
5.Zinc 6.Tin
1.Copper
2.Lead 3.Aluminium
4.Alloys of lead
14/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 15: SOCKET OUTLETS
The socket outlets are provided for temporary electrical connections such as table lamps, table fans, radio, TV, mobile chargers etc.
The socket outlet can be of the following two types:
Two pin type (Live, Neutral)
Three pin type (Live, Neutral, Earth)
15/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 16: PLUGS
The
plugs along with
flexible cords are used for providing the electrical supply to the portable appliances like table fan, table lamps, radio etc.
The plugs are available in two types, similar to the sockets:
Two pin plugs
Three pin plugs
16/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 17: LAMP HOLDER
A lamp holder supports the lamp and connects it to the supply system as well
The lamp holders are classified into following different types:
Batten holders
Angle holder
Pendant holder
Water tight holders
Bracket holders
bracket
17/25
11/22/2025

## Slide 18: CEILING ROSE
The ceiling rose is used for connecting the ceiling fans, pendant lamps etc to the supply system.
Ceiling rose is made of the following two parts:
Base
Cover
18/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 19: SYMBOLS USED IN ELECTRICAL WIRING
Following are the conventional symbols to be used for wiring accessories in wiring plans and drawing of electrical installations.
19/25
Sr. No. | Description | Symbol
1. | Earthing | 
2. | Single pole one way switch | 
3. | Single pole double throw switch (S.P.D.T.) | 
4. | Double pole double throw switch (D.P.D.T.) | 
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 20: SYMBOLS USED IN ELECTRICAL WIRING
20/25
Sr. No. | Description | symbol
5. | Fuse | 
6. | Circuit breaker | 
7. | Two way switch | 
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 21: WIRING AND ACCESSORIES DT-Empathize
21/25
DT Phase | Focus Area | Key Points
Empathize | Users | Home users → safety & ease of use Electricians → easy installation, standard sizes Industries → durability, fire safety Students → clarity & learning of wiring components
 | Pain Points | Loose connections causing sparks Poor-quality accessories overheating Difficulty identifying phase/neutral/earth Switchboards not user-friendly Non-ISI accessories creating hazards
 | User Expectations | ✔ Safe & reliable operation ✔ Shockproof design ✔ Good aesthetics (modular) ✔ Standard color coding ✔ Smooth operation & long life
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 22: WIRING AND ACCESSORIES
DT-Define
22/25
Define | Definition | Wiring accessories are components used to control, connect, protect, and support the electrical wiring system. Examples: Switches, Sockets, Plugs, MCB, RCCB, Connectors, Junction boxes.
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 23
Let’s summarize
23/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 24: REFERENCES
2/25
IS 732 – Electrical Wiring Installation
BIS Standards
NEC (National Electrical Code)
www.howstuffworks.com
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 25
23/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT