## Slide 1: SNS COLLEGE OF TECHNOLOGY
An Autonomous Institution Coimbatore-35
Department of Artificial Intelligence and Data Science
23EET103-Electric Circuits and Electron Devices.
UNIT III :WIRING, GROUNDING AND SAFETY
I B.TECH AIDS / I SEMESTER
Topic 1 : Wiring: General Rules , Materials and
Accessories
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 2: Let’s Recall !!
2/25
What is wiring?
Why do we need rules for safe wiring? Common household wiring components Difference between good and faulty wiring What are electrical materials?
Why are wiring accessories needed in installations?
Basic components used in home wiring
Conductors, insulators, and their importance
Safety devices used in wiring systems
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 3: PUSH BUTTON SWITCH
This type of switch consists of one blade only.
The blade is given a rocking action by press button and movement is controlled by a cam and spring.
13/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 4: FUSES
In any electrical installation, fuse is used for protecting the appliances against over current. Fuse is used in different stages of the wiring.
A fuse can be made of the
conducting
following materials:
5.Zinc 6.Tin
1.Copper
2.Lead 3.Aluminium
4.Alloys of lead
14/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 5: SOCKET OUTLETS
The socket outlets are provided for temporary electrical connections such as table lamps, table fans, radio, TV, mobile chargers etc.
The socket outlet can be of the following two types:
Two pin type (Live, Neutral)
Three pin type (Live, Neutral, Earth)
15/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 6: PLUGS
The
plugs along with
flexible cords are used for providing the electrical supply to the portable appliances like table fan, table lamps, radio etc.
The plugs are available in two types, similar to the sockets:
Two pin plugs
Three pin plugs
16/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 7: LAMP HOLDER
A lamp holder supports the lamp and connects it to the supply system as well
The lamp holders are classified into following different types:
Batten holders
Angle holder
Pendant holder
Water tight holders
Bracket holders
bracket
17/25
11/22/2025

## Slide 8: CEILING ROSE
The ceiling rose is used for connecting the ceiling fans, pendant lamps etc to the supply system.
Ceiling rose is made of the following two parts:
Base
Cover
18/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 9: SYMBOLS USED IN ELECTRICAL WIRING
Following are the conventional symbols to be used for wiring accessories in wiring plans and drawing of electrical installations.
19/25
Sr. No. | Description | Symbol
1. | Earthing | 
2. | Single pole one way switch | 
3. | Single pole double throw switch (S.P.D.T.) | 
4. | Double pole double throw switch (D.P.D.T.) | 
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 10: SYMBOLS USED IN ELECTRICAL WIRING
20/25
Sr. No. | Description | symbol
5. | Fuse | 
6. | Circuit breaker | 
7. | Two way switch | 
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 11: WIRING AND ACCESSORIES DT-Empathize
21/25
DT Phase | Focus Area | Key Points
Empathize | Users | Home users → safety & ease of use Electricians → easy installation, standard sizes Industries → durability, fire safety Students → clarity & learning of wiring components
 | Pain Points | Loose connections causing sparks Poor-quality accessories overheating Difficulty identifying phase/neutral/earth Switchboards not user-friendly Non-ISI accessories creating hazards
 | User Expectations | ✔ Safe & reliable operation ✔ Shockproof design ✔ Good aesthetics (modular) ✔ Standard color coding ✔ Smooth operation & long life
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 12: WIRING AND ACCESSORIES
DT-Define
22/25
Define | Definition | Wiring accessories are components used to control, connect, protect, and support the electrical wiring system. Examples: Switches, Sockets, Plugs, MCB, RCCB, Connectors, Junction boxes.
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 13
Let’s summarize
23/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 14: REFERENCES
2/25
IS 732 – Electrical Wiring Installation
BIS Standards
NEC (National Electrical Code)
www.howstuffworks.com
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT

## Slide 15
23/25
Wiring: General Rules , Materials and Accessories\23EET103\ECED\Ms.RANJANI K \ AP\IOT\SNSCT