## Slide 1
ADDITIVE
MANUFACTURING
From Digital Design to Physical Object
An Introduction for First-Year Engineering Students
3D Printing Layers
UG 1st Year | Introduction to Manufacturing

## Slide 2
What is Additive Manufacturing?
Core Definition
Additive Manufacturing (AM) is a process of creating objects by adding material layer-by-layer from a digital 3D model. Also popularly known as 3D Printing — a term coined in the 1990s.
Digital Blueprint
Starts from a CAD (Computer-Aided Design) file or 3D scan
Layer-by-Layer
Material is deposited, fused, or cured one thin layer at a time
Near-Zero Waste
Material is added only where needed — unlike cutting/drilling
Additive Manufacturing | UG Introduction

## Slide 3
Additive vs. Subtractive Manufacturing
ADDITIVE
(3D Printing)
Material is ADDED layer by layer
Starts from nothing — builds up
Minimal material waste
Complex shapes are easily possible
Ideal for prototyping & custom parts
Slower for mass production
VS
SUBTRACTIVE
(CNC Milling / Turning)
Material is REMOVED from a solid block
Starts from a large raw block
Significant material wasted
Very precise for standard shapes
Ideal for high-volume production
Faster for metal components
Additive Manufacturing | UG Introduction

## Slide 4
How Does Additive Manufacturing Work?
1
3D Modeling
Design the part using CAD software (e.g., SolidWorks, Fusion 360) or scan a real object into a digital model.
2
Slicing
Slicing software (e.g., Cura) divides the 3D model into hundreds of thin horizontal layers (0.1–0.3 mm thick).
3
Printing
The printer builds the object layer by layer — depositing, fusing, or curing material according to each slice.
4
Post-Processing
Remove support structures, clean the surface, sand, paint, or heat-treat the final object as required.
💡 Key Insight: The entire process — from digital file to physical part — can take as little as a few hours!
Additive Manufacturing | UG Introduction

## Slide 5
Types of Additive Manufacturing Processes
Most Common
FDM
Fused Deposition Modeling
Melts plastic filament and extrudes it layer by layer. Most common desktop 3D printer.
High Detail
SLA
Stereolithography
Uses UV laser to cure liquid photopolymer resin. High detail and smooth surface finish.
Strong Parts
SLS
Selective Laser Sintering
Laser fuses powdered nylon or metal. No support structures needed. Strong parts.
Metal Parts
SLM
Selective Laser Melting
Fully melts metal powder (steel, titanium). Used for aerospace and medical implants.
Fast & Scalable
Binder Jet
Binder Jetting
Liquid binding agent is selectively deposited onto powder layers. Fast and scalable.
Fast Resin
DLP
Digital Light Processing
Uses a digital projector to flash a full UV layer at once — faster than SLA for small parts.
Additive Manufacturing | UG Introduction

## Slide 6
Materials Used in Additive Manufacturing
Polymers (Plastics)
PLA — biodegradable, easy to print
ABS — strong, heat-resistant
PETG — flexible & tough
Nylon — wear-resistant, lightweight
Resin (SLA/DLP) — smooth, high detail
Metals
Stainless Steel — durable, corrosion-resistant
Titanium — high strength, biocompatible
Aluminum — lightweight, used in aerospace
Inconel — high-temperature superalloy
Cobalt-Chrome — used in medical implants
Ceramics & Composites
Alumina & Zirconia ceramics
Carbon fibre reinforced polymers
Bioceramics for bone scaffolds
Glass-filled nylon for rigid parts
Continuous fibre composites (Markforged)
Additive Manufacturing | UG Introduction

## Slide 7
Real-World Applications of AM
Healthcare & Medical
Patient-specific surgical implants
Hearing aids & dental crowns
Bio-printed tissue scaffolds
Prosthetic limbs & orthotics
Aerospace & Defence
Lightweight turbine blades
Rocket engine components (SpaceX)
Drone airframes & UAV parts
Satellite structural brackets
Automotive
Rapid prototyping of car parts
Customised interior components
Tooling jigs & fixtures
Lightweight structural inserts
Consumer & Electronics
Custom earbuds & wearables
Phone cases & accessories
Architectural scale models
Personalised jewellery & fashion
Additive Manufacturing | UG Introduction

## Slide 8
Advantages & Limitations
✅ ADVANTAGES
Design freedom — complex geometries impossible with traditional methods
Mass customisation — each part can be unique at no extra cost
Reduced material waste — only material needed is used
Faster prototyping — from design to part in hours
On-demand manufacturing — print anywhere, anytime
Consolidation of assemblies — multiple parts printed as one
⚠️ LIMITATIONS
Slower production speed — not yet ideal for large-scale mass production
Limited material range — fewer options compared to traditional processes
Layer-by-layer structure may cause anisotropic (directional) weakness
Post-processing required — support removal, sanding, finishing
High equipment cost — industrial machines can cost millions
Size constraints — print volume limited by machine build chamber
Additive Manufacturing | UG Introduction

## Slide 9
AM Industry: Growth & Future Trends
$20B+
Global AM market size (2023)
~25%
Annual market growth rate (CAGR)
>50,000
Industrial AM systems installed worldwide
2040
Projected year AM becomes mainstream manufacturing
Emerging Trends & Future Directions
4D Printing
Smart materials that change shape after printing in response to heat, moisture, or light.
Sustainable AM
Recycled filament, biodegradable polymers, and zero-waste metal printing.
AI & Topology Optimization
AI auto-designs parts with maximum strength and minimum material use.
Space Manufacturing
3D printing in microgravity — NASA tests printing tools on the ISS.
Additive Manufacturing | UG Introduction

## Slide 10
KEY TAKEAWAYS
01
AM builds objects layer-by-layer from a 3D digital model — the opposite of cutting or drilling.
02
Key processes: FDM, SLA, SLS, SLM — each suited for different materials and applications.
03
Materials range from cheap PLA plastic to titanium and biocompatible ceramics.
04
Used in aerospace, medicine, automotive, and consumer products across the globe.
05
AM excels in design freedom, customisation, and prototyping — but is still limited in speed and cost for mass production.
WHAT'S NEXT?
Try CAD modelling: TinkerCAD (free & beginner-friendly)
Explore slicing software: Download Ultimaker Cura (free)
Visit your college's fabrication lab — most have FDM printers
Watch: 'How 3D Printing Will Change the World' — TED Talk
Read: ASTM F2792 — Standard Terminology for AM
Thank You | Questions Welcome