## Slide 1: Computer Networks and Data Communications
UNIT I

## Slide 2: NETWORK TYPES
LAN
MAN
WAN

## Slide 3: A Communications Model
Source
  generates data to be transmitted
Transmitter
  Converts data into transmittable signals
Transmission System
  Carries data
Receiver
  Converts received signal into data
Destination
  Takes incoming data

## Slide 4: Simplified Communications Model - Diagram

## Slide 5: Simplified Data Communications Model

## Slide 6: Networks
A network consists of two or more computers that are linked in order to share resources (such as printers and CDs), exchange files, or allow electronic communications.

## Slide 7: Simplified Network Model

## Slide 8: Wide Area Networks
simplest form, a wide-area network (WAN) is a collection of local-area networks (LANs) or other networks that communicate with one another. A WAN is essentially a network of networks, with the Internet the world's largest WAN.
Alternative technologies/ types
  Circuit switching
  Packet switching
  Frame relay
  Asynchronous Transfer Mode (ATM)

## Slide 9: Circuit Switching
It is the process of exchanging information between two communication devices.
There are two types of switching: circuit switching and packet switching.
e.g. telephone network

## Slide 11: Packet Switching
Data sent out of sequence
Small chunks (packets) of data at a time
Packets passed from node to node between source and destination
Packet switching is the transfer of small pieces of data across various networks. These data chunks or “packets” allow for faster, more efficient data transfer.

## Slide 13: Frame Relay
Frame Relay (frame relay) is a packet switching technology that fragmented into transmission units called frames and sent in high-speed bursts through a digital network. Establishes an exclusive connection during the transmission period called virtual connection.

## Slide 15: Asynchronous Transfer Mode
ATM stands for Asynchronous transfer mode. It is a switching technique used by telecommunication networks that uses asynchronous time-division multiplexing to encode data into small, fixed-sized cells. ATMs can be used for efficient data transfer over high speed data networks.

## Slide 17: Protocol Architecture
Task of communication broken up into modules
For example file transfer could use three modules
  File transfer application
  Communication service module
  Network access module

## Slide 18: Simplified File Transfer Architecture

## Slide 19: Protocols in Simplified Architecture

## Slide 20: TCP/IP Protocol Architecture
Developed by the US Defense Advanced Research Project Agency (DARPA) for its packet switched network (ARPANET)
Used by the global Internet
No official model but a working one.
  Application layer
  Host to host or transport layer
  Internet layer
  Network access layer
  Physical layer

## Slide 21: Physical Layer
Physical interface between data transmission device (e.g. computer) and transmission medium or network
Characteristics of transmission medium
Signal levels
Data rates
etc.

## Slide 22: Network Access Layer
Exchange of data between end system and network
Destination address provision
Invoking services like priority

## Slide 23: Internet Layer (IP)
Systems may be attached to different networks
Routing functions across multiple networks
Implemented in end systems and routers

## Slide 24: Transport Layer (TCP)
Reliable delivery of data
Ordering of delivery

## Slide 25: Application Layer
Support for user applications
e.g. http, SMPT

## Slide 26: TCP/IP Protocol Architecture Model

## Slide 27: OSI Model
Open Systems Interconnection
Developed by the International Organization for Standardization (ISO)
Seven layers

## Slide 28: OSI Reference Model
The OSI model defines seven layers:
Layer 7: Application Layer
Layer 6: Presentation Layer
Layer 5: Session Layer
Layer 4: Transport Layer
Layer 3: Network Layer
Layer 2: Data Link Layer
Layer 1: Physical Layer

## Slide 29: OSI Layers
Application
Presentation
Session
Transport
Network
Data Link
Physical

## Slide 31: OSI v TCP/IP

## Slide 32
At the bottom of our OSI model we have the Physical Layer, which represents the electrical and physical representation of the system. This can include everything from the cable type, radio frequency link (as in a Wi-Fi network), as well as the layout of pins, voltages, and other physical requirements.
Physical Layer (Layer 1):

## Slide 33
Data Link Layer (Layer 2):
The Data Link Layer provides node-to-node data transfer (between two directly connected nodes), and also handles error correction from the physical layer. Two sublayers exist here as well--the Media Access Control (MAC) layer and the Logical Link Control (LLC) layer.

## Slide 34
Network Layer (Layer 3):
Its most basic sense, this layer is responsible for packet forwarding, including routing through different routers.
  Example: IP

## Slide 35
Transport Layer (Layer 4):
The Transport Layer deals with the coordination of the data transfer between end systems and hosts. How much data to send, at what rate, where it goes, etc. The best known example of the Transport Layer is the Transmission Control Protocol

## Slide 36
Session Layer (Layer 5):
When two computers or other networked devices need to speak with one another, a session needs to be created, and this is done at the Session Layer. Functions at this layer involve setup, coordination (how long should a system wait for a response, for example) and termination between the applications at each end of the session.

## Slide 37
Presentation Layer (Layer 6):
The Presentation Layer represents the area that is independent of data representation at the application layer. In general, it represents the preparation or translation of application format to network format, or from network formatting to application format.
  Data conversion into application format
  Encryption/decryption

## Slide 38
Application Layer (Layer 7):
The Application Layer in the OSI model is the layer that is the “closest to the end user”. It receives information directly from users and displays incoming data to the user.
  Everything is application specific
  Example: File Transfer, Electronic Mail

## Slide 39: Multimedia
Multimedia is a set of more than one media element used to produce a concrete and more structured communication method. In other words, multimedia is the simultaneous use of data from different sources. These sources in multimedia are known as media elements.
Elements of Multimedia
Text, Audio, video, pictures, animations, etc.