## Slide 1
An Autonomous Institution Coimbatore-45
DEPARTMENT OF INFORMATION TECHNOLOGY
23ITT304 Information Coding Technique
Unit IV
SYNDROME DECODING
P.Thilagarani AP/IT
SNS COLLEGE OF TECHNOLOGY
LINEAR BLOCK CODES AND CYCLIC CODES

## Slide 2
SYNDROME DECODING
Efficient Error Correction for Data Transmission
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 2/14

## Slide 3
STARTER
🔑
RECALL & CONNECTION
Before we dive in, let us recall: Linear Block Codes use parity check bits to ensure data integrity.
Icebreaker: If you were sending a vital bank transfer and one bit flipped from '0' to '1', how would the receiver know it wasn't valid?
Key point
The objective today is to master the 'Syndrome'— the fingerprint that identifies exactly where an error occurred.
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 3/14

## Slide 4
EMPATHIZE: THE PERSONA
Meet Rohan, Network Engineer
Rohan works at a 5G infrastructure firm in Bangalore. His system receives millions of packets per second.
The Pain Point: Comparing received vectors to every single valid codeword (Minimum Distance Decoding) is too slow. He needs a shortcut to find errors without exhaustive searching.
Example
The 'Define' phase: How can we identify errors instantly using only the Parity Check Matrix (H)?
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 4/14

## Slide 5
THE IDEATE PHASE: THE SYNDROME
Instead of checking every codeword, we calculate the Syndrome (S) using the received vector r and the transpose of the Parity Check Matrix H.
Why it works:
If S = 0, the received vector is a valid codeword. If S ≠ 0, an error has occurred!
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 5/14

## Slide 6
PROTOTYPE: DECODING STEPS
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 6/14

## Slide 7
🧠
VERTICAL DEPTH: MATHEMATICAL RIGOR
The Properties
The syndrome depends only on the error pattern, not the sent codeword.
For a single error in position i, the syndrome will be identical to the i-th column of H.
Remember
If two different error patterns yield the same syndrome, they belong to the same 'Coset'. We always choose the 'Coset Leader' with the minimum weight.
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 7/14

## Slide 8
FUTURE SCOPE
HORIZONTAL BREADTH: APPLICATIONS
Where is it used?
Deep Space: Voyager 1 uses variations of this to send photos across the solar system.
QR Codes: Error correction allows you to scan a damaged or partially covered code.
RAM: ECC (Error Correction Code) memory in servers uses syndrome-style checks to prevent crashes.
Quantum Error Correction uses 'Stabilizer Codes', which are quantum versions of syndrome decoding.
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 8/14

## Slide 9
TEST: THE DECODING SEQUENCE
Arrange the steps of the Syndrome Decoding process in the correct order for a received vector 'r'.
Extract data bits from the corrected codeword v
Compute Syndrome S = r · Hᵀ
Subtract/XOR the Error Pattern from r (v = r - e)
Identify the Error Pattern (e) corresponding to S
Answers on the next slide...
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 9/14

## Slide 10
TEST: THE DECODING SEQUENCE
Arrange the steps of the Syndrome Decoding process in the correct order for a received vector 'r'.
Compute Syndrome S = r · Hᵀ
1.
Identify the Error Pattern (e) corresponding to S
2.
Subtract/XOR the Error Pattern from r (v = r - e)
3.
Extract data bits from the corrected codeword v
4.
✅​
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 10/14

## Slide 11
SUMMARY MIND MAP
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 11/14

## Slide 12
REFLECT & APPLY
Imagine you are designing a communication system for a high-interference industrial plant in Pune. If the noise is so high that two bits flip simultaneously, but your Syndrome Decoding only targets single-bit errors, what happens to the data? How would you solve this?
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 12/14

## Slide 13
REFLECT & APPLY
You might have said...
The syndrome points to a 'false' single-bit error, causing a corrupted message.
We must increase the 'minimum distance' by adding more parity bits.
We must expand the Syndrome Table to include two-bit error patterns.
✅​
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 13/14

## Slide 14
Thank You
12.05.2026 23ITT304-INFORMATION CODING TECHNIQUES | SYNDROME DECODING | P.Thilagarani | SNSCT 2/14