## Slide 1
An Autonomous Institution Coimbatore-35
DEPARTMENT OF INFORMATION TECHNOLOGY
23ITT304 Information Coding Techniques
Unit V
CONVOLUTIONAL CODES AND APPLICATIONS
UNLOCKING INFORMATION CODING
P.Thilagarani AP/IT
SNS COLLEGE OF TECHNOLOGY
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 2/14

## Slide 2
UNLOCKING INFORMATION CODING
Mastering Trellis Diagrams for Reliable Communication.
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 2/14

## Slide 3
ICEBREAKER
🔑
WARM-UP: THE NOISE CHALLENGE
Imagine sending a critical binary message across a crowded room. Static and interference (noise) flip your 1s to 0s.
Discussion: How can we ensure the receiver gets the exact original message without repeating it ten times?
Key point
Convolutional coding adds 'memory' to the data, making it resilient to errors.
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 3/14

## Slide 4
DESIGN THINKING: EMPATHIZE
THE ENGINEER'S PERSONA
Meet Arjun, a Network Engineer
Arjun works on 5G infrastructure in Mumbai. His challenge is maintaining high data speeds in dense urban areas where signals bounce off buildings.
The Core Problem: How do we decode complex, interleaved signals efficiently in real-time?
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 4/14

## Slide 5
IDEATE
FROM STATE MACHINES TO TRELLIS
To solve Arjun's problem, we move from a static State Diagram to a Trellis Diagram.
While a state diagram shows what can happen, a Trellis shows when it happens by expanding the state machine over time.
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 5/14

## Slide 6
VERTICAL DEPTH
🧠
ANATOMY OF A TRELLIS
Technical Components
Nodes: Represent the current state of the encoder memory.
Branches: Represent the transitions between states based on input bits.
Labels: Typically written as 'Input / Output' (e.g., 1 / 11).
Remember
The number of states is 2^(K-1), where K is the constraint length.
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 6/14

## Slide 7
THE VITERBI DECODING PROCESS
The Trellis enables the Viterbi Algorithm to find the 'Shortest Path' via Hamming distances.
Calculate Metrics: Compare received bits against all possible branch labels.
Accumulate & Prune: Keep the path with the lowest cumulative error; discard others.
Traceback: At the end, follow the 'survivor path' backward to decode.
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 7/14

## Slide 8
HORIZONTAL BREADTH
BEYOND WIRELESS: BROAD APPLICATIONS
Trellis-coded modulation isn't just for cellular data. It's used in:
Deep Space Comm: Communicating with Mars rovers.
Hard Drives: Reading magnetic data accurately.
Voice Recognition: Hidden Markov Models (HMMs) use similar structures.
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 8/14

## Slide 9
ACTIVITY: SURVIVE THE NOISE
Group Problem Solving
Form groups of three.
You are given a received sequence: 11 01 10.
Using the provided 4-state Trellis, calculate the Hamming distance for the first two transitions.
Identify: Which path is more likely to be the survivor?
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 9/14

## Slide 10
🔍
LESSON SUMMARY
Key Takeaways
Memory: Trellis diagrams visualize encoders with memory.
Efficiency: The Viterbi algorithm prevents exponential complexity.
Reliability: Essential for modern high-speed digital comms.
Example
Think of the Trellis as a roadmap where 'Noise' represents roadblocks, and Viterbi is your GPS finding the most likely route.
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 10/14

## Slide 11
FINAL ASSESSMENT
What is the primary advantage of a Trellis Diagram over a standard State Diagram in coding theory?
1.
It uses less power to transmit.
2.
It explicitly shows the passage of time and sequence of states.
3.
It eliminates the need for any redundant parity bits.
4.
It can only be used for block codes, not convolutional codes.
Answers on the next slide...
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 11/14

## Slide 12
FINAL ASSESSMENT
What is the primary advantage of a Trellis Diagram over a standard State Diagram in coding theory?
1.
It uses less power to transmit.
2.
It explicitly shows the passage of time and sequence of states.
👍​
3.
It eliminates the need for any redundant parity bits.
4.
It can only be used for block codes, not convolutional codes.
✅​
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 12/14

## Slide 13
5.04.2026 INFORMATION CODING TECHNIQUES | UNLOCKING INFORMATION CODING| P.Thilagarani | SNSCT 2/14
Thank You